## Slide 1
CCE 313 - Computer Networks
ICMP Pinger Lab: Network Diagnostics Tool
Prosenjit Mondol
ID: 2102049 | Reg: 10176
B.Sc. CSE, 5th Semester
November 10, 2025

## Slide 2
Introduction & Problem Statement
INTRODUCTION
• Network performance monitoring is critical for reliable communication
• ICMP (Internet Control Message Protocol) - fundamental for diagnostics
PROBLEM STATEMENT
Network administrators need tools to:
  • Measure network latency and round-trip time (RTT)
  • Detect packet loss and network congestion
  • Monitor network stability and jitter
  • Visualize real-time network performance
IMPORTANCE IN NETWORKING
• Quality of Service (QoS) monitoring for SLA compliance
• Network troubleshooting and performance optimization
• Real-time diagnostics for instant network health feedback

## Slide 3
ICMP Protocol Architecture (RFC 792)
ICMP OVERVIEW - Network Layer (Layer 3)
• Error Reporting: Unreachable destinations, TTL exceeded
• Diagnostic Functions: Echo Request/Reply (Ping)
• Network Control Messages: Redirect, Source Quench
ICMP PACKET STRUCTURE (Echo Request/Reply)
┌─────────────────────────────────┐
│ IP Header (20 bytes) │
├─────────────────────────────────┤
│ Type (8 bits) - Request:8/Reply:0│
├─────────────────────────────────┤
│ Code (8 bits) - 0 │
├─────────────────────────────────┤
│ Checksum (16 bits) │
├─────────────────────────────────┤
│ Identifier (16 bits) │
├─────────────────────────────────┤
│ Sequence Number (16 bits) │
├─────────────────────────────────┤
│ Data (Variable) │
└─────────────────────────────────┘

## Slide 4
Implementation Methodology
THREE-TIER IMPLEMENTATION APPROACH
1. RAW SOCKET IMPLEMENTATION (Scapy)
  • Full control over ICMP packet structure
  • Requires administrator privileges
  • packet = IP(dst=host) / ICMP(type=8, code=0)
2. WINDOWS ICMP API (No Admin Required)
  • Windows IP Helper API (iphlpapi.dll)
  • IcmpSendEcho function for echo requests
  • Works without elevated privileges
3. SUBPROCESS FALLBACK (Cross-Platform)
  • Platform-native ping commands
  • Maximum compatibility across OS
  • Regex parsing for RTT extraction
ARCHITECTURE: User Input → ICMPPinger → Implementation
Selection → Results Processing → GUI Update

## Slide 5
Advanced Features & Components
REAL-TIME PERFORMANCE MONITORING
• Live RTT Graphing (Matplotlib Integration)
  - Dynamic plotting of latency trends
  - Color-coded success/failure indicators
COMPREHENSIVE STATISTICS DASHBOARD
• Minimum/Maximum/Average RTT
• Jitter (network stability metric)
• Packet Loss % and Success Rate %
MULTI-TAB GUI INTERFACE (Tkinter)
• Ping Client Tab: Configuration and execution
• Echo Server Tab: Simulated server responses
• Statistics Tab: Detailed analytics and CSV export
KEY FEATURES
✓ No Admin Required (Windows API fallback)
✓ Cross-Platform Support (Windows/Linux/Mac)
✓ Thread-Safe Operation | ✓ Export Capabilities

## Slide 6
Analysis & Results
TEST SCENARIO
Target: 8.8.8.8 (Google DNS) | Count: 20 | Interval: 1s | Timeout: 10s
SAMPLE RESULTS
─────────────────────────────
Minimum RTT: 12.34 ms
Maximum RTT: 45.67 ms
Average RTT: 23.45 ms
Jitter: 8.92 ms
Packet Loss: 0.0%
Success Rate: 100.0%
ANALYSIS INSIGHTS
• Low Packet Loss (0%) → Stable network connection
• Moderate Jitter (8.92ms) → Acceptable variation
• Average RTT (23.45ms) → Good connection quality
REAL-WORLD IMPLICATIONS
• Network Health Assessment for SLA compliance
• Troubleshooting congestion | Route optimization
• Application Performance (VoIP/Gaming require <50ms)

## Slide 7
Practical Implementation
1. SCAPY IMPLEMENTATION
packet = IP(dst=host) / ICMP(seq=seq_num)
response = sr1(packet, timeout=10.0)
if response.getlayer(ICMP).type == 0:
  rtt_ms = (end_time - start_time) * 1000
2. WINDOWS ICMP API
handle = iphlpapi.IcmpCreateFile()
iphlpapi.IcmpSendEcho(handle, addr, data,
  size, None, reply_buf, buf_size, timeout)
reply = ICMP_ECHO_REPLY.from_buffer(reply_buf)
rtt = reply.RoundTripTime
3. SUBPROCESS FALLBACK
cmd = ['ping', '-n', '1', '-w', '10000', host]
output = subprocess.run(cmd, capture_output=True)
match = re.search(r'time[=<]\s*([\d\.]+)\s*ms', output)
rtt = float(match.group(1))

## Slide 8
Network Performance Metrics
STATISTICAL CALCULATIONS
1. Round-Trip Time (RTT) Analysis
  • Min, Max, Average RTT calculations
  • RTT_avg = (1/n) × Σ RTT_i
2. Jitter Calculation (Network Stability)
  • Jitter = (1/n-1) × Σ |RTT_(i+1) - RTT_i|
3. Packet Loss Percentage
  • Packet Loss = (Failed / Total) × 100%
PERFORMANCE INTERPRETATION
RTT: Excellent <20ms | Good 20-50ms | Fair 50-100ms
Jitter: Excellent <5ms | Good 5-20ms | Fair 20-50ms
Loss: Excellent 0% | Good <1% | Fair 1-5%
EXPORT FORMAT: CSV with metrics, values, and units

## Slide 9
Challenges & Solutions
TECHNICAL CHALLENGES ENCOUNTERED
1. Permission Issues (Raw Sockets)
  Challenge: Raw socket creation requires admin privileges
  Solution: Implemented Windows ICMP API fallback
  Result: Works without administrator rights on Windows
2. Cross-Platform Compatibility
  Challenge: Different OS-specific implementations
  Solution: Multi-tier fallback (Scapy → API → Subprocess)
  Result: Seamless operation across Windows/Linux/macOS
3. Thread Safety in GUI Updates
  Challenge: Matplotlib updates causing conflicts
  Solution: Used canvas.draw_idle() and Tkinter.after()
  Result: Smooth real-time graph updates
BEST PRACTICES
✓ Graceful degradation | ✓ Comprehensive error handling
✓ Resource management | ✓ Real-time user feedback

## Slide 10
Conclusion & Summary
KEY ACHIEVEMENTS
• Implemented three approaches for ICMP echo requests
• Developed GUI with live RTT graphing and statistics
• Created cross-platform solution (Windows/Linux/macOS)
• Built practical network diagnostic tool
MAIN TAKEAWAYS
• ICMP is essential for network layer diagnostics
• Multi-tier implementation ensures reliability
• Statistical analysis provides actionable insights
• GUI-based tools make diagnostics accessible
PROJECT OUTCOMES
✓ Functional ICMP ping client (3 methods)
✓ Real-time RTT visualization
✓ Comprehensive statistics (min/max/avg/jitter/loss)
✓ Export capabilities (CSV reports)
FUTURE ENHANCEMENTS
• Traceroute integration | • Wireshark integration
• Multiple host monitoring | • Historical data trending

## Slide 11
References
TECHNICAL DOCUMENTATION
• RFC 792 - Internet Control Message Protocol
  https://tools.ietf.org/html/rfc792
• Forouzan, B. A. (2012)
  Data Communications and Networking, 5th Edition
  McGraw-Hill Education
• Kurose, J. F., & Ross, K. W. (2021)
  Computer Networking: A Top-Down Approach, 8th Edition
  Pearson Education
IMPLEMENTATION LIBRARIES
• Scapy Documentation: https://scapy.readthedocs.io/
• Python ctypes Module
• Windows IP Helper API (Microsoft Docs)
PROJECT RESOURCES
GitHub: https://github.com/pronad1/Socket_Programming
Email: prosenjit1156@gmail.com

## Slide 12
Thank You! 🎓
Questions & Discussion
Prosenjit Mondol
ID: 2102049 | Reg: 10176
Contact: prosenjit1156@gmail.com
GitHub: https://github.com/pronad1